## Slide 1: NZOTS-STM and –SAM
STM = Subtropical (macronutrient-limited); SAM = Subantarctic (micronutrient-limited)
Moorings deployed October 2000-May 2012, ~3000 m water depth
Biophysical parameters:
  T, S, DO, currents (0-200 m); satellite surface chla (SSC)
  Particle fluxes (1500 m) – mass, POC, PON, PP, BSi, Ca→CaCO3, Al→lithogenic, forams, pteropods, dinofl. cysts, radiolarians
References: Nodder et al. (2016) JGR-Oceans (accepted)
Prebble et al. (2013) Marine Micropal. 104: 25–37.
NZ Contact: Scott.Nodder@niwa.co.nz

## Slide 2
High interannual variability at both sites
Lower fluxes at SAM cf. STM
Annual cycles extracted from 2000-12 flux data-set
  High spring biomass & direct fluxes at STM
  Delayed translation of autumnal bloom to depth at STM
  High summer biomass at SAM not matched by high fluxes
  High spring fluxes at SAM
Annual cycles for satellite chla, total mass flux and particulate organic carbon flux; Solid blue dots indicates high data confidence; green dashed line = ±1 stdev for surface chla; yellow dots = ±1 stdev for 1500 m fluxes
Annual cycle of chla & MLD from satellite and CTD
High spring fluxes at SAM derived from subsurface production not observed by satellites
SSC = satellite surface chla; C0 = 0-5 m Σchla from CTD chla-fluorescence; Ctot = 0-300 m Σchla; MLD = mixed-layer depth