## Slide 1: Data QC and best practices
Louise darroch, justin buck (BODC, NOC)

## Slide 2: About me
Data manager at the British Oceanographic Data Centre (BODC) in the UK

## Slide 3: Best practices Q & A
Q1. Is the data format capable of encoding a variety of QC protocols?
Yes!
….and no

## Slide 4: QC protocols
Global attributes
Coordinate variables
Data variables
Yes !
QC in Oceansites NetCDF
Provenance
QC_indicator
Processing_level
Type, name, dimension, attributes
LATITUDE:QC_indicator = ;
LATITUDE:uncertainty = ;
LATITUDE:processing_level = ;
Type, name, dimension, attributes
TEMP_QC:long_name =; TEMP_QC:conventions =; TEMP_QC:coordinates =; TEMP_QC:flag_values =; TEMP_QC:flag_meanings =;
TEMP_uncertainty:long_name = ; TEMP_uncertainty:units =; TEMP_uncertainty:_FillValue = ; TEMP_uncertainty:comment =;
Optional
Mandatory
Mandatory
Either
Describes overall dataset quality
Describes data channel quality
Describes data cycle quality

## Slide 5: QC protocols
Data cycle flags
Reference table 2

## Slide 6: QC protocols
Processing level descriptors
Reference table 3

## Slide 7: More info on QC indicators in data format
http://www.oceansites.org/documents/

## Slide 8: QC protocols
No
Reference standard QC procedures (best practices)?

## Slide 9: Example standard QC procedures
http://coaps.fsu.edu/woce/docs/qchbook/qchbook.htm
Flagging protocol
Time tests
Bound tests
Platform speed tests
Calculations (e.g. true wind)

## Slide 10: Example standard QC procedures
http://www.argodatamgt.org/Documentation
Flagging protocols
CTD pressure tests
Pressure and salinity adjustments
Protocols for near-real time and delayed-mode data

## Slide 11: Example standard QC procedures
http://www.fixo3.eu/
QC procedures

## Slide 12: Best practices Q & A
Q2. Is there data in OceanSITES, not currently QC’d at all and if so is this a DMT issue or Steering Team issue?

## Slide 13: Best practices Q & A
Q2. Is there data in OceanSITES…?
Is there data not currently QC’d at all…?
Yes!
What | Number | %
Total | 31150 | 
QC’d |  | 
Not QC’d |  | 
Err..

## Slide 14: Best practices Q & A
Q2. …..and if so is this a DMT issue or Steering Team issue?
Steering team
or

## Slide 15: Best practices Q & A
Q2A. Should the data format checker be checking all mandatory fields….?
….if so, is it?
Yes!
No
Available at http://www.coriolis.eu.org/Data-Products/Tools
Used by GDACs to check data
Should check any version of NetCDF sent
Should have documentation

## Slide 16: Best practices Q & A
Q3. Perspective/challenges from AtlantOS

## Slide 17: Optimising and Enhancing the Integrated Atlantic Ocean Observing Systems
GOSHIP
SOOP
CRP
Fish + plankton
ARGO
OceanSites
Glider
Surface drifter
Sea Floor mapping
Observing networks
Harmonise
Atlantic dataset
Standardised QC procedures
quality

## Slide 18: Key observing variables
Domain | GCOS Essential Climate Variables (ECV) | 
Atmospheric (over land, sea and ice) | Surface: | Air temperature, Wind speed and direction, Water vapour, Pressure, Precipitation, Surface radiation budget.
 | Upper-air: | Temperature, Wind speed and direction, Water vapour, Cloud properties, Earth radiation budget (including solar irradiance).
 | Composition: | Carbon dioxide, Methane, and other long-lived greenhouse gases[3], Ozone and Aerosol, supported by their precursors.
Oceanic | Surface: | Sea-surface temperature, Sea-surface salinity, Sea level, Sea state, Sea ice, Surface current, Ocean colour, Carbon dioxide partial pressure, Ocean acidity, Phytoplankton
 | Sub-surface: | Temperature, Salinity, Current, Nutrients, Carbon dioxide partial pressure, Ocean acidity, Oxygen, Tracers.
Terrestrial | Terrestrial: | River discharge, Water use, Groundwater, Lakes, Snow cover, Glaciers and ice caps, Ice sheets, Permafrost, Albedo, Land cover (including vegetation type), Fraction of absorbed photosynthetically active radiation (FAPAR), Leaf area index (LAI), Above-ground biomass, Soil carbon, Fire disturbance, Soil moisture.
Domain | GOOS Essential Oceanographic Variables (EOV)
Physics | Temperature (Surface, Interior), Salinity (Surface, Interior), Currents. (Surface, Interior), Sea Surface Height, Sea Ice, Sea State, Ocean Surface Vector Stress (new), Sensible and Latent Heat Fluxes (proposed)
Biogeochemistry | Oxygen, Inorganic Macro Nutrients, Carbonate System, Transient Tracers, Suspended Particles, Nitrous Oxide, Carbon Isotope (13C), Dissolved Organic Carbon
Biology | Under development
GCOS Essential Climate Variables
GOOS Essential Ocean Variables

## Slide 19: Data harmonisation and discovery
Controlled vocabularies
https://www.bodc.ac.uk/data/codes_and_formats/vocabulary_search/

## Slide 20: Data harmonisation and discovery
Controlled vocabularies
https://www.bodc.ac.uk/data/online_delivery/nodb/search/

## Slide 21: Data harmonisation and discovery
Data vocabulary matrix

## Slide 22: Data harmonisation and discovery
SeaDataNet 2 EU project
44 data centres
Common vocabularies
Common format (CDI)
http://www.seadatanet.org/

## Slide 23: Data harmonisation and discovery
http://www.seadatanet.org/
http://www.bodc.ac.uk

## Slide 24: Thank you